## Slide 1: Rear Upright CDR
Mike Ornstein
11/6/2012

## Slide 2: Bearing Selection: Prime Option
SKF 61817-2RZ (85mm bore, 0.27kg (0.15kg in front) – 0.59lb)
  Deep groove

## Slide 3: Bearing Selection: Alt Option
KB035XP0*RBC (3.5” bore, 0.27lb)
  X-type Thin Section

## Slide 4: Solid Model
Rear: 2.06lbs
Front: 2.18lbs
Old: 1.85lbs

## Slide 5: Engineering Drawing
Coming Soon

## Slide 6: General Modeling Conditions
Cases:
  Turning (max lateral g -> normal/lateral patch loads)
  Braking (max braking forces)
Model:
  Element size 0.1”, bearings bonded to upright
  Spherical joints at all real life places
Deflections include Suspension Links

## Slide 7: Turning
Forces applied at contact patch
  Peak normal load from load transfer
  Peak lateral load from max cornering
12.5ksi peak stress (at clevis fillet)
0.02 deg toe change
0.01 deg camber change

## Slide 11: Braking
Peak forces experienced during braking
  Longitudinal due to contact patch friction
  Caliper on Upright
  Spindle reaction on Upright from Caliper
16.5ksi peak stress (at lower a-arm pickup)
0.28 deg toe change
  Due to soft toe link
0.02 deg camber change